## Slide 1: Compliance in Commercial Facilities
28th October 2019

## Slide 2
What is building compliance:
Statutory building compliance and commercial property compliance is a complex set of regulations, assessments and inspections that all businesses need to undertake to comply with current government legislation.
Health and Safety legislation requires employers to carry out servicing, maintenance, testing and statutory inspections, referred to as maintenance or statutory inspection herein on its properties to ensure the health, safety and welfare of its employees, visitors, contractors and members of the public.

## Slide 3
Critical Compliance Areas:
Fire
Lifts
Electrical
Gas
Water
Asbestos
Air Conditioning
Other – Compliance / Insurance / Best Practice

## Slide 4
Fire
The Regulatory Reform Order 2005 requires that all aspects of fire safety are managed by a ‘responsible person’ i.e. business owner, manager or employer. This individual needs to ensure that all fire systems are inspected and checked regularly in order to comply with relevant British Standards, fire risk assessments are carried out, staff are trained and fire emergency evacuation routes planned.
What do you need:
An appointed responsible person
Fire Risk Assessment
Completed remedial and recommendations following the Risk Assessment
Passive and active fire maintenance
Maintenance Record in a Fire Log Book
Weekly Fire Alarm test (documented)
Fire Evacuation plan & a yearly fire evacuation test (documented)
Fire Damper test and inspection
Fire Wardens
A maintenance schedule for the inspection of fire appliances e.g. Portable Fire Extinguishers, Hose Reels and Fire Blankets
Emergency Light Testing
Weekly Fire Signage / Escape route / External Staircase / Fore stopping checks (documented)

## Slide 5
Lifts
The Lifting Operations and Lifting Equipment Regulations 1998 (LOLER) introduced
new requirements for the safe provision and use of lifting equipment. Regulation 9
of LOLER requires that all lifts provided for use in work activities are thoroughly
examined by a competent person at regular intervals.
If you are a lift owner or someone responsible for the safe operation of a lift used
at work, such as a facilities manager or supervisor, you are a ‘duty holder’ under
LOLER. This means that you have a legal responsibility to ensure that the lift is
thoroughly examined and that it is safe to use.
What do you need:
Check the Lift phone / alarm works weekly and document it
Service the lift at least every 12 months and keep the records
Inform your insurer there is a lift at the property (they may request you get it inspected)

## Slide 6
Electrical
The Electricity at Work Regulations (EAWR) 1989 (1991 in Northern Ireland) are made under the Health and Safety at Work Act 1974
Employers as ‘duty holders’ must provide a safe working environment with regard to all electrical equipment and systems, regardless of when they were manufactured, installed or brought into use
All electrical systems must be maintained in a safe condition and an important aspect of such maintenance is periodic inspection and testing
What do you need:
Portable appliance testing including a leak test of microwaves
5Y Fixed wired test certificate
Completed remedial and recommendations following the 5Y Test
Generation / UPS / CHP test and inspection ( if applicable )
RCD Testing of sockets

## Slide 7
Gas
Gas regulations (The Gas Safety Regulations 1998) states that all gas systems must be checked regularly (at least annually) to ensure they are safe. This includes safe installation, servicing, inspection and certification for all types of gas equipment. These must be carried out by registered gas-safe engineers.
What do you need:
A gas service every 12 months that results in an issued gas safe certificate (CP12)
Completed remedial and recommendations following the service
This applies to all gas equipment – Kitchens / Boilers etc

## Slide 8
Water
All water systems must have a valid Legionella Risk Assessment (these stay valid for 2 years), to ensure that the risk of legionella is reduced. Many businesses are also required to carry out monthly testing of water temperatures to check that water is kept at an optimum temperature to avoid any water borne diseases. The Control of Substances Hazardous to Health Regulations 1988 requires that employers reduce workers exposure to any hazardous substances, including those borne in water. Employers are responsible for determining what health hazards there are in the workplace, carrying out risk assessments and providing information, instruction and training for employees. REF: ACOPL8 - Legionnaires’ disease
Part 2: The control of legionella bacteria in hot and cold water systems
An appointed responsible person
Legionella Risk Assessment
An up to date schematic diagram of your water system
Completed remedial and recommendations following the risk assessment
Water log book containing the results of monitoring, inspection and any checks carried out; this include monthly temperature testing and the flushing of any outlets not regularly used ie Sinks / Showers etc.
Tank cleaning ( if applicable)
Calorifier / Expansion vessel test and inspection ( if applicable)
Thermostatic Mixing Valves test and inspection ( if applicable)

## Slide 9
Asbestos
This guidance is for, anyone who is responsible for maintenance and repairs in a building, which may contain asbestos. The ‘duty to manage’ asbestos is included in the Control of Asbestos Regulations 2012.
Was the building built or refurbished before 2000?
No, asbestos is unlikely to be present – no action required.
If the answer is YES, an asbestos survey detailing if asbestos is present is required
If asbestos is present you will need:
Appointed a duty holder
Asbestos risk assessment & survey
Signage showing where the asbestos is
Implement an Asbestos register
Keep records of regular checks
Note: Anyone who may work on asbestos must be trained and use safe working methods. Most work with asbestos needs to be done by a licensed contractor and all contractors must be made aware asbestos is present.

## Slide 10
Air Conditioning
Under The Energy Performance of Buildings Regulations 2007, air conditioning systems must undertake regular energy inspections. The regularity of these depends on the weight and number of units, so:
Every 12 months – buildings over 3kg refrigerant, usually 1 – 15 air conditioning units Every 6 months – buildings over 30kg refrigerant, usually 15 – 75 air conditioning units Every 3 months – buildings over 300kg refrigerant, usually more than 75 air conditioning units
The inspections must be carried out by an approved inspector, and should take into account design, installation and operation of the system.
Records must be stored and up to date

## Slide 11
Other Compliance Considerations (if applicable):
Man safe / Fall arrest roof systems – PUWER
Folding Door Maintenance – PUWER
Lighting Protections system - BS EN 62305-3 / BS EN 62305-4
Petrol Interceptors - PPG3, BSEN 858
Oil/ Diesel Tank Inspections - DSEAR
Display Energy Certificate & Energy Performance Report - England and Wales of the European Directives 2002/91/EC and 2010/31/EU on the Energy performance of buildings
Kitchen and Ventilation Duct clean and inspection – TR19
Auto door - ACOP L24 Regulation 5, Regulation 18. Supply of Machinery (Safety) Regulations 2008. BS 7036-0: 2014. BS EN 16005:2012
Legal or Insurance Compliance:
CCTV servicing – GDPR
Access Control & Intruder system maintenance – Insurance Requirement
Disabled pull cord testing / Hearing Loop induction Servicing – Equality Act 2010

## Slide 12
What to do next :
1. Carry out an audit using the template provided
2. Establish gaps
3. Understand the regulation
4. Understand your duty and responsibility
3. Put together a compliance plan
4. Order the required services
Please click the icon

## Slide 13
Reference guides:
Fire - http://www.legislation.gov.uk/uksi/2005/1541/contents/made
Lifts - http://www.hse.gov.uk/pUbns/priced/loler.pdf
Electrical - http://www.hse.gov.uk/pUbns/priced/hsr25.pdf
Gas - http://www.hse.gov.uk/pubns/books/l56.htm and http://www.hse.gov.uk/pUbns/priced/l56.pdf
Water - http://www.hse.gov.uk/pubns/priced/hsg274part2.pdf
Asbestos - http://www.hse.gov.uk/asbestos/enforcement.htm
Air Conditioning - https://www.gov.uk/government/publications/air-conditioning-inspections-for-buildings
Equipment (Moving doors / walls)- http://www.hse.gov.uk/work-equipment-machinery/puwer.htm
Lightning Protection - http://www-public.tnb.com/eel/docs/furse/BS_EN_IEC_62305_standard_series.pdf
Dangerous Substances - http://www.hse.gov.uk/fireandexplosion/dsear.htm
Energy - https://eur-lex.europa.eu/LexUriServ/LexUriServ.do?uri=OJ:L:2010:153:0013:0035:EN:PDF & https://eur-lex.europa.eu/LexUriServ/LexUriServ.do?uri=OJ:L:2003:001:0065:0071:EN:PDF

## Slide 14
Reference guides:
Ventilation - https://www.thebesa.com/knowledge/shop/products/tr19-grease-specification-for-fire-risk-management-of-grease-accumulation-within-kitchen-extraction-systems/
Auto doors - http://www.hse.gov.uk/pubns/priced/l24.pdf Regulation 5
GDPR - https://www.gov.uk/government/publications/guide-to-the-general-data-protection-regulation
Equality Act - https://www.gov.uk/guidance/equality-act-2010-guidance